## Slide 4
Define and Verify Component

## Slide 5
Define and Verify Production System

## Slide 6
Design and Implement Production Method

## Slide 7
Design and Implement Production Method
Step 3
PFMEA
Process Control Plan
Characteristics Matrix
Quality Standards and Specifications
Stage Drawings/Models
Tooling & Fixturing

## Slide 8
CAPP Reference
Reference Part
Product Family Template (reference) – Capability Intranet
MSA Minitab GR&R
PFD
DFMEAs
Stage MBD / BCT
SAP- Concessions History
Inspection Plan
Quality History O,D ratings
DCM
Global Reference PFMEAs
PFMEA
CP
Data capture form
CAPP
Engineering MBD
Process specific PFD
Statistical Process Control
3DTI
MES
(Manual)
Future BiQ Flow

## Slide 9
Characteristics Matrix – Current state
Launch TcE and Nx, Generate TCG
In drafting mode import a dwg sheet and align with origin
MPOS numbering using BCT move bubble for proper positions
Any correction in the BCT excel table before export into DCM template
Assign project id and save in ipxml and PDF
Extract into DCM template
Check section A and align correct each column for the DWG requirements for page 1
Repeat step 8 for the remaining pages
Prepare for filling MOM (TI, CMD, IPS, standards and RQSC)
Refer above documents and fill MOM and inspection methods for each features
Peer review
Rework
Delivery and communicate to counterpart
Work Flow
Method & Tools
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
TcE, NX
NX
BCT
BCT
BCT
BCT
Excel
Excel
Excel
Excel
Excel
Excel
Email
Process Time -
RFT -
Future state
Flow diagram
Time Calculation
Input
Design Drawing
Design Drawing
Stage Drawings/Process

## Slide 10
Characteristics Matrix – Future state
Launch TcE and Nx, Generate TCG
In drafting mode import a dwg sheet and align with origin
MPOS numbering using BCT move bubble for proper positions
Any correction in the BCT excel table before export into DCM template
Assign project id and save in ipxml and PDF
Extract into DCM template
Check section A and align correct each column for the DWG requirements for page 1
Repeat step 8 for the remaining pages
Prepare for filling MOM (TI, CMD, IPS, standards and RQSC)
Refer above documents and fill MOM and inspection methods for each features
Peer review
Rework
Delivery and communicate to counterpart
Work Flow
Method & Tools
Manual
Manual
Automatic
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
Manual
TcE, NX
NX
BCT
BCT
BCT
BCT
Excel
Excel
Excel
BCT
BCT
BCT
TcE
Process Time -
RFT -
Obsolete
Not necessary
Not necessary
Need to automate through BCT, CAPP
Current state
Flow diagram

## Slide 11
Current State Design - DCM